## Slide 1: Technical Memo 1-2 2016 Yields
15 November 2016

## Slide 2: TM-1-2 Tasks
Review of updated RiverWare models
Incorporation of 2016environmental flows developed by Espey/Carollo team
Development of demand scenarios that
  Identify the location of potential demands
  Develop operational criteria to meet those demands
Additional modeling

## Slide 3: Riverware Model Review
SBG and USACE using different versions and assumptions
  (flood operations versus yield estimating)
Reviewed multiple versions of the USACE Model
Tech memo defining standard set of inputs and assumptions for future runs
Memo Provided as Attachment A of TM1-2
Notes: USACE was running model with different hydrology and assumptions and was getting different results. Developed a tech memo that identified the standard set of inputs and assumptions, as well as identifying alternatives to those assumptions and recommendations about how to document those differences.

## Slide 4: Differences from Previous Modeling
New environmental flows
Minor update to Lake Ralph Hall hydrology
No scenarios with summer release of 86 cfs release from Patman
Some scenarios with new Patman senior to Marvin Nichols
Notes: SB3 based eflows instead of Lyons flows
Minor changes to LRH flows early in modeling period
After consulting with USACE, now making a constant 10 cfs minimum release (new eflows only apply to reallocated storage/new diversions)

## Slide 5: Environmental Flows – Marvin Nichols
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Average 2016 Eflows | 22943.9114 | 25520.5505 | 27143.013 | 24120.511 | 23675.4858 | 17978.3439 | 1807.9595 | 1383.2529 | 4790.8652 | 7671.8221 | 9487.1919 | 20679.7192
Lyons Eflows | 4191.5391 | 5687.4151 | 11712.4476 | 6963.3696 | 9409.1969 | 4163.1994 | 892.8263 | 413.5453 | 494.0805 | 496.0146 | 1416.364 | 3270.6075
Notes: Considerable variation in new eflows depending on hydrologic condition
Blue line is the average monthly volume reserved by eflows. Some times actual eflows are considerably less, some times it is more.
On average these eflows are considerably greater than Lyons and have resulting in a corresponding reduction in yield

## Slide 6: Environmental Flows – Wright Patman
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Average 2016 Eflows | 43772.5232 | 47646.1936 | 51278.9081 | 37997.7718 | 38302.7012 | 28229.3316 | 1528.9032 | 1345.3396 | 7480.8926 | 12433.6757 | 17570.2595 | 36675.6029
Lyons Eflows | 87755.1074 | 60335.6033 | 154044.8926 | 91434.0496 | 16583.2066 | 26598.3471 | 8411.5041 | 5902.8099 | 5712.3967 | 11633.4545 | 16256.5289 | 62569.7851
Notes: Eflows applied only to new reallocated storage and new diversions from Patman
10 cfs minimum always applies
Considerable variation in new eflows depending on hydrologic condition
Blue line is the average monthly volume reserved by eflows. Some times actual eflows are considerably less, some times it is more.
Much lower than Lyons in Jan, Mar and April, so corresponding increase in yield

## Slide 7: Yields – Patman Reallocation (New)
Chart: New Yield (acre-feet per year)
| 232.5 ft | 242.5 ft
2016 Yield | 153253 | 304883
Lyons Yield | 131700 | 287445
Does not include 180,000 ac-ft currently authorized from Patman
Notes: This is only new yield. Does not include 180K of current water rights

## Slide 8: Yields – Marvin Nichols
Chart: Yield (acre-feet per year)
| 328 ft
2016 Yield | 392297
Lyons Yield | 464200
Notes: Did not run 313.5 with new eflows because yield was too low

## Slide 9: Yields – Combinations
Chart: Yield (acre-feet per year)
| 2016 Yield | Lyons Yield | 2016 Yield | Lyons Yield
2016 New Patman | 80807 | 226786
2016 Nichols | 379836 | 379256
Lyons Patman | 50886 | 186629
Lyons Nichols | 464228 | 464199
Does not include 180,000 ac-ft currently authorized from Patman
Notes: Only 242.5/328 scenario meets supply goals for project

## Slide 10: Yields – New Patman Senior to Nichols
Chart: Yield (acre-feet per year)
| Nichols Senior | New Patman Senior | Nichols Senior | New Patman Senior
Patman | 80807 | 226786
Nichols | 379836 | 379256
Patman | 151080 | 303796
Nichols | 286887 | 261096

## Slide 11: Demand Scenarios
Summarized in TM1-1
  Scenario 1 – In-basin demands only
  Scenario 2 – Adds demands adjacent to basin
Chart: Demand (acre-feet per year)
| Scenario 1 | Scenario 2
2070 Demands | 93706 | 281078
In-Basin Reserve | 120800 | 120800
Notes: Two scenarios in TM-1
These are the 2070 demands
Black line is 20% of goal supply of 604,000 ac-f/yr (120,800 ac-ft/yr)
Conclusion – there will be enough supply to meet in-basin demands plus some extra

## Slide 12: Yield with “Alternative” Operation
Chart: Yield (acre-feet per year)
| Priorrity Operation | Patman/ Nichols | Priorrity Operation | Patman/ Nichols
Patman | 80807 | 226786
Nichols | 379836 | 379256
Alternative Operation | 496824 | 638425
Notes: This demonstrates operation of Patman and Nichols to meet demands rather than as individual projects using priority operation. AKA system operation. If operated in concert to meet these demands, over 30,000 additional acre-feet of water can be generated.

## Slide 13: Summary
New environmental flows
  Reduce yield of Nichols
  Increase yield of Patman
  Reduce combined yield of Patman and Nichols
20% reserve for in-basin needs should be sufficient to meet all in-basin needs plus some additional water for out-of-basin
Holistic operation of Patman/Nichols to meet demand could increase yield from system

## Slide 14: Questions?